## Slide 1: Post Harvest Technology
Dr. Anurag Nema
Assistant Professor
Department of Post Harvest Engg. and Tech.
Anand Agricultural University, Anand
E-mail: dranuragnema@aau.in

## Slide 2: Post-harvest technology/Post-harvest management
Post-harvest technology/Post-harvest management is interdisciplinary science and technique applied to agricultural produce after harvest for its production, conservation, processing, packaging, distribution, marketing and utilization to meet the food and nutritional requirements of the people in relation to their needs.
Post-harvest processing is directed to the conservation of produce, process goods and value adding to make the material more readily usable and economically more remunerative.
The post-harvest technology is gaining importance for increasing agricultural productivity and growers intend to become producer-cum-processor by utilizing the technologies of processing.

## Slide 3: Cont’d…
Post-harvest technology involves all treatments or processes that occur from time of harvesting until the foodstuff reaches the final consumer.
Efficient techniques for harvesting, conveying/transportation, handling, storage, processing/preservation, packaging, marketing and utilization etc. are components of the postharvest chain.

## Slide 4: Activities involved in the post-harvest system
Technical activities: harvesting, field drying, threshing, cleaning, additional drying, storage, processing.
Economic activities: transporting, marketing, quality control, nutrition, extension, information and communication, administration and management.

## Slide 5: Importance of post-harvest technology/processing
Reduction of post-harvest losses.
Maintain or enhance quality of the products and make it readily marketable.
Reduction of cost of production.
Reducing malnutrition.
Economic loss reduction.
Availability.
Employment generation.
Post-harvest technology has potential to create rural industries.
Export earnings.

## Slide 6: Stages of a whole post-harvest system
Harvesting (Handling)
Threshing
Drying (transport and distribution)
Storing
Processing: (i) Primary – cleaning, classification, dehulling, grinding, packaging, soaking, winnowing, drying, sieving, milling (ii) Secondary – mixing, cooking, heating (pasteurization, sterilization, blanching), cooling (freezing), frying, cutting, extrusion
Product evaluation (quality control: standard recipes)
Packaging (weighing, labelling, sealing)
Marketing (publicity, selling, distribution)
Use (recipes elaboration: traditional dishes, new dishes)
Consumer preferences (product evaluation, consumer education)

## Slide 7: Post-harvest losses
In developing countries, where nearly 40-60% of food lost occurs at the production, processing and postharvest stages.
Depending on the crop, between 15 and 35% of food may be lost before it even leaves the field.
According to the Agriculture Ministry, INR 50,000 crores worth of food produced is wasted every year in India.

## Slide 8: Factors affecting postharvest losses
Pre-harvest production practices
Harvesting and field handling
Packing or packaging
Storage
Transport
Market handling
Perishability of the produce.

## Slide 9: Pre-harvest production practices
Water supply (irrigation)
Soil fertility (use of fertilizers)
Cultivation practices
Use of agro chemicals (pesticides and herbicides)

## Slide 10: Harvesting and field handling
Quality cannot be improved after harvest, only maintained.
Harvest should be completed during the coolest time of the day and produce should be kept shaded in the field.
Handling should be done carefully and gently.
Training harvest labor to handle the crop gently
Harvesting at proper maturity
Harvesting dry whenever possible
Handling each fruit or vegetable no more than necessary (field pack if possible)
Installing padding inside bulk bins and avoiding over or under-packing of containers
Harvesting damage can be prevented by:

## Slide 11: Packing or packaging
For the most part, the preparation of produce for market is carried out in a packing house
Pack house handling includes: sorting, cleaning and washing, fungicide treatment, quality selection and grading
Suitable packages and handling techniques can reduce the amount of damage to which fresh produce is exposed during marketing
Packaging should be designed to prevent physical damage to produce and be easy to handle

## Slide 12: Storage
Temperature is the single most important factor in maintaining quality after harvest.
Refrigerated storage retards the following elements of deterioration in perishable crops: (i) aging due to ripening, softening and textural and color changes (ii) undesirable metabolic changes and respiratory heat production (iii) moisture loss (iv) spoilage due to invasion by bacteria, fungi and yeasts, undesirable growth such as sprouting of potatoes.

## Slide 13: Transportation
Transportation is a big and often the most important factor in the marketing of fresh produce
Ideally, transport would take produce from the grower directly to the consumer
Losses directly attributed to transport conditions can be high
The damage and loss incurred during non-refrigerated transport are caused primarily by mechanical damage and by overheating

## Slide 14: Causes of mechanical damage
Careless handling of packed produce during loading and unloading
Vibration (shaking) of the vehicle, especially on bad roads
Fast driving and poor condition of the vehicle
Packages stacked too high; the movement of produce within a package increases in relation to its height in the stack
Causes of overheating
The use of closed vehicles without ventilation
Close-stow stacking patterns blocking the movement of air between and through packages, thus hindering the dispersal of heat
The lack of adequate ventilation of the packages themselves
Exposure of the packages to the sun while awaiting transport or while trucks are queuing to unload at their destination

## Slide 15: Market handling
Improper handling may cause damages to crops, especially perishable products
Perishability of the produce
The products which are more perishable are more sensitive to post-harvest damages